## Slide 1: Arbitrary Order Total Variation for Deformable Image Registration By Jinming Duan, Xi Jia, Joseph Bartlett, Wenqi Lu, Zhaowen Qiu published on Science direct, 2023
Presented by:
Lior Dvir and Neta Becker
Notes: The alternating direction method of multipliers (ADMM) is an algorithm that attempts to solve a convex optimization problem by breaking it into smaller pieces, each of which will be easier to handle.

## Slide 2: Table of contents 01 03 02 04
Background
Our Method
Paper
Results

## Slide 3: Background
The paper aims to solve non-rigid registration in medical imaging
It utilizes TV of arbitrary order in its regularization which:
  Induces smooth solutions
  Allows discontinuities in local deformation fields
  Is less dependent on initial alignment
Background
=

## Slide 4: Image registration
Image registration: the process of matching two or more images of the same or similar object, viewpoints, or imaging modalities.
Rigid transformation: Objects are rotated and translated with respect to one another
Non-Rigid transformation: correspondence between objects is achieved with localized stretching of the images
Background

## Slide 5: The proposed algorithm
The authors want to find that minimizes the following equation: where:
is the 2D displacement field
are the input images
is the n’th order distributional derivative of u. n is an arbitrary integer.
* The authors use the intensity consistency constraint (the intensity at point x in the target image is the same as that at point x+u in the source image)
Paper
Notes: In summary, to handle the original non-linear, non- differentiable and non-convex minimization problem (1) , we break it down into a warping problem (2a) and a linearized, convex minimization problem (2b) . We then develop an acceler- ated, ADMM-based iterative algorithm to decompose (2b) into an over-relaxation step and three simple subproblems. Each subprob- lem has a closed-form, point-wise solution and can be efficiently handled using existing numerical methods (i.e. DCT and soft thresholding). As such, the algorithm is very accurate and efficient, which can be confirmed in Section 4.3 .

## Slide 6: Paper’s results
Image is deformed
Affine transformation
1a
1b
1c
2a
2b
2c
Paper
From left to right:
Using 1st order TV
Using 1st order TV
Using 3rd order TV

## Slide 7: Our goal
Video tracking is the process of locating a moving object over time using a camera.
Our goal is to develop an algorithm that performs object tracking of objects that may change their form throughout the video.
Our Method

## Slide 8: Implementation (algorithm)
For the first frame:
Detect the object of interest using object detection algorithm
Create a mask of said object
For any frame that follows:
Use the algorithm from the given article to shape the mask using the current frame and the previous one as input images
Create a mask according to the result of the algorithm
Our Method

## Slide 9: Implementation (algorithm)
Our Method

## Slide 10: Results
Results

## Slide 11: Results
Results
Original Video
Ground Truth
Algorithm Masking

## Slide 12: Comparison with another algorithm
Comparisons
Our model
Works on any given object
Robust – can handle changes in the shape of the object
Works slow. Takes a few minutes for the algorithm to run
Compared model
Works with tennis balls in RGB only
Doesn’t handle changes in the shape of the object well
Works fast. It takes a few seconds for the algorithm to run
The mentioned algorithm was written by Adrian Rosebrock

## Slide 13: Thank you!
Questions?